## Slide 1
Actually in real life what we simulate in the simulators we don't get exactly that in the physical design.So as every thing is probabilistic you have to ensure that the chipyou fabricate should work in all process corners.
if the functionality is achieved in all specs then u have to simulate in Slow-Slow corner to figure out the worst case speed.Similarly for power spec u simulate in FF corner as in that corner the Current is maximum as the transistors have low Vt there.
Fast means operation fastly which reasons from thin gate oxide or other fabrication variation.
TT - Typical NMOS, Typical PMOS S - slow F - fast
SS/TT/FF/SF/FS make chip corners, which directly determines your yield

## Slide 2
Process corners are, in a way, an attempt to put the bound on what comes out of the foundry—what’s the fastest something can happen, what’s the slowest, what’s the worst power, what’s the least power?
Typical Corners: • FF (fast fast) • SF (slow fast) • SS (slow slow) • FS (fast slow) • TT (typical typical)
One naming convention for process corners is to use two-letter designators, where the first letter refers to the N-channel MOSFET (NMOS) corner, and the second letter refers to the P channel (PMOS) corner.
Fast and slow corners exhibit carrier mobilities that are higher and lower than normal, respectively. For example, a corner designated as FS denotes fast NFETs and slow PFETs.
A corner designated as FS denotes fast NFETs and slow PFETs.
The first three corners (TT, FF, SS) are called even corners, because both types of devices are affected evenly, and generally do not adversely affect the logical correctness of the circuit. The resulting devices can function at slower or faster clock frequencies, and are often binned as such.
The last two corners (FS, SF) are called "skewed" corners, and are cause for concern. This is because one type of FET will switch much faster than the other, and this form of imbalanced switching can cause one edge of the output to have much less slew than the other edge
To account for process variations, an IC designer not only has to design for good electrical performance, but also design for high manufacturing yield.
There are many factors that effect yield. Physical problems that are highly layout dependent effect yield. Manufacturability issues such as defect density on the silicon, maturity of the process, and effectiveness of design rules also effect yield
the output current, load reg, etc will all change as the PMOS changes strong or weak.
Fast in the sense is carrying higher currents than normal

## Slide 3
The SPICE model parameters, are listed below, usually changed for corner analysis (for N- and P-MOST). TOXM, DXL, DXW, DELVTO, CJ, CJSW, CJGATE, CGDO, CGSO.
Another factor, and the main topic of this paper, is how the design will react to process, temperature and supply voltage variations. The design's sensitivity to these variations is called parametric yield. Increasing parametric yield is a challenge that is within a designer's realm.
There are currently several tools, or analyses, that a designer may use to check the design for process, temperature and voltage variations. This paper provides a brief description of the commonly used methods, including corners simulation, Monte Carlo analysis, and response surface modeling
Corners simulation is perhaps the most widely used method to test for process, temperature and voltage variations. With this method, a designer determines the worst case corners, or conditions, under which the design will be expected to function.
each corner is simulated, and the output of each corner is examined to determine whether or not the design performs as required under each of the specified conditions.
running as many relevant corners as possible increases the robustness of the design and therefore is likely to increase the parametric yield
the best case is HIGH VCC, LOW TEMPERATURE and LOW PMOS/NMOS threshold voltage (FF)
1. Mobility variation due to implantation of N+ and P+ 2. Vth variation 3. Resistance of the actives 4. Body coefficient 5. Oxide thickness Other parameters like the effective Length, effective width, Cjsw caps, Cj caps also change. Hence Slow Slow, Fast Fast corners come into picture

## Slide 4
The temperature Sweep deature is used to analyze the circuit at each temperature in a specified range, producing a series a curves, one for each temperature setting.